## Slide 1
AI + AR POWERED AUTOMOBILE LEARNING SYSTEM
AutoLearnAR
Component-Wise System Presentation — mapping the 4-module AI/AR design to the actual Android application
1
Vision-Based Component ID
2
Task Recognition
3
AR Verification & Guidance
4
Evaluation & Safety
Source: AutoLearnAR_Project (Android / Kotlin) + system design documentation

## Slide 2
OVERVIEW
What this deck covers
The original design describes 4 AI/AR components. Every one of them is implemented in the app — this deck shows exactly how, file by file.
01
Overall system architecture
How a student's session flows across screens, models and data
02
Component 1 – Vision-Based Component Identification
Camera frame → on-device CNN → identified engine part
03
Component 2 – Student Task Recognition
Matches the component to a task, then tracks the student's live actions
04
Component 3 – AR Verification & Instruction
AR overlays, motion guidance, audio coaching, live step verification
05
Component 4 – Evaluation & Safety Feedback
Scoring, component-specific safety rules, history & grading
06
Implementation map & tech stack
Every class file placed against the component it belongs to
AutoLearnAR – Component-Wise System Overview
2

## Slide 3
OVERALL ARCHITECTURE
End-to-end mapping: student session → 4 AI/AR components
Home Screen
Student starts
a session
Camera
Capture
CameraX live
preview
Component
Identification
MLClassifier
(TFLite CNN)
1
Component
Detail Screen
Name, function,
specs shown
Task
Recognition
TaskRecognizer +
action model
2
AR
Verification
Spatial3DEngine +
PartGuidanceEngine
3
Evaluation &
Safety
Score +
SafetyData
4
“Try Again” → retry AR Verification
“Review Theory” → back to Library / Chatbot
score saved
SUPPORTING MODULES — reachable throughout the session
Library /
Theory Content
LibraryScreen →
TheoryDetailScreen
AI Chatbot
Gemini API – grounded
in the theory content
Account &
History
ScoreHistoryManager – saves
every attempt locally
AutoLearnAR – Component-Wise System Overview
3

## Slide 4
1
COMPONENT 1
Vision-Based Engine Component Identification
“What part is the student looking at?” — on-device image classification
Camera Frame
CameraX preview
(CameraScreen.kt)
MLClassifier
TFLite MobileNetV2
224×224 input
Confidence ≥ 60%?
AppNavigation.kt
confidence gate
Normalize +
Lookup
match ID in
EngineData.kt
Component Detail
Screen
name, function,
specs, confidence %
below threshold → “move closer, try again”
WHAT IT DOES
Identify the engine component the student's camera is pointed at, in real time, without needing an internet connection.
HOW IT WORKS IN THE APP
CameraX streams a live preview (CameraScreen.kt / CameraPreview.kt); the student captures a frame.
MLClassifier.kt loads a TensorFlow Lite MobileNetV2 model (component_model.tflite + labels.txt) and runs on-device inference — resize to 224×224, build an RGB float buffer, one forward pass, softmax over all labels.
The top label is accepted only if confidence ≥ 60% (AppNavigation.kt); below that the student is asked to move closer and retry.
The accepted label is normalized and matched to a full EngineComponent record (id, name, function, specifications) from EngineData.kt, then shown on ComponentScreen.kt together with the detection confidence.
KEY IMPLEMENTATION FILES
ai/MLClassifier.kt
ai/ComponentDetector.kt (interface)
ai/DemoComponentDetector.kt (offline stub)
ui/CameraScreen.kt, ui/CameraPreview.kt
ui/ComponentScreen.kt
data/EngineData.kt, model/EngineComponent.kt
CORE TECHNOLOGY
CameraX · TensorFlow Lite 2.16 · MobileNetV2 CNN · Kotlin Coroutines
AutoLearnAR – Component-Wise System Overview
4

## Slide 5
2
COMPONENT 2
Student Task Recognition
“What is the student trying to do, and which step are they on?”
STATIC TASK LOOKUP
Identified
Component ID
from Component 1
TaskRecognizer.kt
matches componentId →
TaskData.kt / EngineData.kt
Task + Ordered
Steps
shown on
TaskRecognitionScreen.kt
LIVE ACTION RECOGNITION (during practice)
Live Camera
Frame
captured continuously
in VerificationScreen.kt
TFLiteClassifier
action-recognition CNN
(air_filter_action_model)
mapActionToStepIndex()
predicted action →
expected step index
To Component 3
AR Verification &
Instruction
WHAT IT DOES
Turn an identified component into a concrete maintenance task with ordered steps, then continuously track which step the student is actually performing.
HOW IT WORKS IN THE APP
Static lookup: TaskRecognizer.kt matches the identified componentId against curated Task objects (id, componentId, name, ordered steps) from TaskData.kt / EngineData.kt — shown on TaskRecognitionScreen.kt.
Live recognition: a second, dedicated TFLite CNN (TFLiteClassifier.kt, action_labels.txt) classifies what the student's hands/tools are doing in each camera frame (e.g. unclipping, lifting) while they practice.
mapActionToStepIndex() and isExpectedActionForStep() (in VerificationScreen.kt) turn that prediction into a yes/no: “does this action match the step the student should be on right now?” — the rule-based + ML pattern-matching layer from the design doc.
KEY IMPLEMENTATION FILES
ai/TaskRecognizer.kt, model/Task.kt
data/TaskData.kt, data/EngineData.kt
data/PracticalJobData.kt
ui/TaskRecognitionScreen.kt
ui/TFLiteClassifier.kt (action model)
ui/VerificationScreen.kt (step logic)
CORE TECHNOLOGY
Rule-based task matching · TensorFlow Lite action-recognition CNN · Sequence / step-pattern logic
AutoLearnAR – Component-Wise System Overview
5

## Slide 6
3
COMPONENT 3
AR-Supported Task Verification & Instruction
Comparison + AR overlay + optional audio guidance, live on the camera feed
PartGuidanceEngine
per-step mask +
IdentifiedPart + directive
Spatial3DEngine
3D→2D projection
(rotation + perspective)
Compose Canvas
Overlay
highlight mask, arrow
path, on-screen label
TextToSpeech
spoken step directive
+ verified confirmation
3-second Hold
Verification Loop
action must match step
continuously to advance
LIVE SCORE INPUTS TRACKED THROUGHOUT → handed to Component 4
Completion 40%
Time 25%
Stability (avg. confidence) 20%
Precision (reset count) 15%
WHAT IT DOES
Overlay live AR guidance on the camera feed, tell the student exactly what to do next, and confirm — visually and continuously — that they actually did it.
HOW IT WORKS IN THE APP
PartGuidanceEngine.kt supplies, per component and per step, a colored 3D bounding-box mask plus an IdentifiedPart with a 3D anchor point, a motion type (unclip-arc, lift-up, inspect-rotate, press-down) and a plain-language action directive.
Spatial3DEngine.kt projects those 3D points onto the 2D camera view with a real perspective/rotation transform — drawing the highlight mask and an animated motion-path arrow (this stands in for ARCore/ARKit pose tracking).
Android TextToSpeech speaks each step's directive and its “verified” confirmation — the optional audio-guidance module from the design.
The predicted action must match the current step continuously for 3 seconds before auto-advancing; while this runs, 4 live metrics feed straight into Component 4's score.
KEY IMPLEMENTATION FILES
ui/VerificationScreen.kt (main orchestrator)
ai/Spatial3DEngine.kt
ai/PartGuidanceEngine.kt
ui/TFLiteClassifier.kt
ui/ARScreen.kt (earlier AR canvas prototype)
CORE TECHNOLOGY
Jetpack Compose Canvas · Custom 3D→2D projection math · TensorFlow Lite · Android TextToSpeech
AutoLearnAR – Component-Wise System Overview
6

## Slide 7
4
COMPONENT 4
Practical Evaluation & Safety Feedback
Turning a verification run into a graded report, with real safety warnings
Verification Results
steps verified, time,
resets, avg. confidence
SafetyData.kt
safetyRules[componentId] –
real per-part safety warnings
Scoring Engine
weighted formula (live) +
EvaluationEngine.kt (rule-based)
EvaluationScreen.kt
score, grade, mistakes,
safety warnings, suggestions
ScoreHistoryManager
saves ScoreRecord –
score, grade A+–D, date
“Try Again”
returns to AR
Verification (Component 3)
“Review Theory”
loops back to Library /
AI Chatbot
WHAT IT DOES
Score the student's attempt, surface component-specific safety warnings, and keep a persistent history so progress can be tracked over time.
HOW IT WORKS IN THE APP
The live weighted score (Completion 40 + Time 25 + Stability 20 + Precision 15, capped 20–100) computed during verification is the score shown to the student; EvaluationEngine.kt (completed ÷ total steps) exists as a simpler rule-based fallback.
data/SafetyData.kt holds real, component-specific safety rules (e.g. battery: never bridge terminals — hydrogen gas risk; coolant: never open a hot pressurized cap) pulled by componentId.
EvaluationScreen.kt renders the final score, letter grade, missed/skipped steps, safety warnings and suggestions — with Try Again, Review Theory (loops back into theory/chatbot) and Finish actions.
ScoreHistoryManager.kt persists every attempt (task, score, duration, date, grade A+–D) locally so HistoryScreen.kt can show progress over time.
KEY IMPLEMENTATION FILES
ai/EvaluationEngine.kt
model/Evaluation.kt
utils/ScoreCalculator.kt
data/SafetyData.kt
ui/EvaluationScreen.kt
data/ScoreHistoryManager.kt
CORE TECHNOLOGY
Weighted scoring algorithm · Safety-rule lookup engine · SharedPreferences / JSON local persistence
AutoLearnAR – Component-Wise System Overview
7

## Slide 8
IMPLEMENTATION MAP
Every component, traced to its code
# | Component | Purpose | Key Classes | Core Technology
1 | Vision-Based Component ID | Identify the engine part from a camera frame | MLClassifier.kt ComponentDetector.kt | TensorFlow Lite MobileNetV2 CNN
2 | Student Task Recognition | Match component → task, track the live action | TaskRecognizer.kt TFLiteClassifier.kt | Rule-based matching + TFLite action CNN
3 | AR Verification & Instruction | AR overlay, audio guidance, live step check | Spatial3DEngine.kt PartGuidanceEngine.kt | Compose Canvas + 3D→2D projection
4 | Evaluation & Safety Feedback | Score the attempt, surface safety rules | EvaluationEngine.kt SafetyData.kt | Weighted scoring + safety-rule engine
All 4 modules are wired together through AppNavigation.kt, which owns the shared session state (selected component, selected task, verification results) as the student moves through the flow.
AutoLearnAR – Component-Wise System Overview
8

## Slide 9
TECH STACK
What the app is actually built with
UI & Navigation
Jetpack Compose · Navigation Compose · Material 3
Camera
CameraX (camera-core, camera2, lifecycle, view)
On-device AI
TensorFlow Lite 2.16 – two CNN models: component ID (MobileNetV2) + live action recognition
AR Rendering
Custom Compose Canvas drawing + hand-built 3D→2D perspective projection (Spatial3DEngine.kt)
Audio Guidance
Android TextToSpeech (step directives + verification confirmations)
Conversational AI
Google Gemini API via OkHttp – chatbot grounded in the task's theory content
Persistence
SharedPreferences + JSON – score history (ScoreHistoryManager.kt)
Concurrency
Kotlin Coroutines – async inference, live verification loop
AutoLearnAR – Component-Wise System Overview
9

## Slide 10
4 components. 1 architecture.
Thank You
From design document to working Android app — every AI/AR module in the spec has a matching, working implementation in AutoLearnAR.
AutoLearnAR – Component-Wise System Overview
10